## Slide 1: Topic 7:Memory interfacing and Address Decoding
By Omoruyi O.

## Slide 2: Topic
Memory, Types and Notes
Memory Interfacing
Address Decoding.
I/O Interfacing: Memory mapped I/O, Isolated I/O, bus timing, I/O instructions.

## Slide 3: Memory
With regards to Semi-conductor memories, they are devices and circuits that can store data or program.
Memories for data are stored in Volatile units called Random Access memory (RAM).
Memories for program are stored in persistent units called Read-only Memory (ROM).

## Slide 4: Memory notes
A memory device can be viewed as a single column table:
  Table index (row number) refers to the address of the memory.
  Table entries refer to the memory contents or data.
  Each table entry is referred as a memory location or as a word.
Both the memory address and the memory contents are binary numbers, expressed in most cases in Hex format.
The size of a memory device is specified as the number of memory locations times the width or word size (in bits). For example see inset memory table

## Slide 5: Memory notes
Pertaining microprocessors, memory devices or memory chips are often connected with three types of lines : Address, Data, and Control.
Address Lines: The input lines that select a memory location within the memory device. Decoders are used inside the memory chip to select a specific location. The number of address pins on a memory chip specifies the number of memory locations.
If a memory chip has 13 address pins (A0 to A12), then it has: 213 = 23 X 210 = 8K locations.

## Slide 6: Data Lines
6
Data Connections: All memory devices have a set of data output pins (for ROM devices), or input/output pins (for RAM devices).
  Most RAM chips have common bi-directional I/O connections.
  Most memory devices have 1, 8 or 16 data lines.

## Slide 7: Control Connection
Enable Connections:
  All memory devices have at least one Chip Select (CS) or Chip Enable (CE) input, used to select or enable the memory device.
    If a device is not selected or enabled then no data can be read from, or written into it.
    The CS or CE input is usually controlled by the microprocessor through the higher address lines via an address decoding circuit.
Control Connections:
  RAM chips have two control input signals that specify the type of memory operation: the Read (RD) and the Write (WR) signals.
    Some RAM chips have a common Read/ Write (R/W) signal.
  ROM chips can perform only memory read operations, thus there is no need for a Write (WR) signal.
    In most real ROM devices the Read signal is called the Output Enable (OE) signal.

## Slide 8: Memory Interfacing
8086 has a 20 bit address bus and hence it can address 220 or 1,048,576 addresses. In each location a byte is stored. So when a word is stored in the memory, it is stored in two consecutive memory locations. Strictly speaking, both memory read and memory write operations require more than one memory cycle. The basic operation of reading/writing a byte from/to a memory location/a port is called a machine cycle. A machine cycle is made up of many states.
If we want the 8086 to complete a memory read and memory write operations to be completed with one machine cycle, the memory is to be organized in the form of two banks. Each bank will have 524,288 bytes each.

## Slide 9: Diagram of Data bus model

## Slide 10: Memory interfacing (continued)
One memory bank contains all the even addressed locations like 00000, 00002 and 00004. The data lines of this bank are connected to the lower eight data lines, D0 through D7 of the 8086. The other memory bank has all the odd addressed locations like 00001, 00003 and 00005. The data lines of this bank are connected to the upper eight data lines, D8 through D15 of the 8086. Address line A0 is used as part of the enabling for memory in the lower bank.
Address lines A1 through A19 are used to select the desired memory device in the bank to address the desired byte in the service. These address lines from A1 through A19 are also used to access a particular location in the upper bank. An additional signal called Bus High Enable (BHE –Active Low) is used to enable the upper memory bank. An external latch, strobed by ALE, grabs the BHE (Active Low) signal that holds it stable for the rest of the machine cycle.

## Slide 11: Table showing bus cycles and memory access

## Slide 12: Bus cycle explained
A bus cycle defines the basic operation that a microprocessor performs to communicate with external devices. Examples of bus cycles are memory read, memory write, input/output read and input/output write.

## Slide 13: Data transfer

## Slide 14: Data Transfer

## Slide 15: Data transfer (16 bit or word transfer)

## Slide 16: 16 bit Data bus odd word transfer

## Slide 17: Memory read
A memory read operation is carried out in the following steps:
  The processor loads on the Address bus the address of the memory location to be read (Step 1).
    Some of the address lines select the memory devices that owns the memory location to be read (Step 1a), while the rest point to the required memory location within the memory device.
  The processor activates the Read (RD) signal (Step 2).
    The selected memory device loads on the data bus the content of the memory location specified by the address bus (Step 3).
  The processor reads the data from the data bus, and resets the RD signal (Step 4).

## Slide 18: Memory write
A memory write operation is carried out in the following steps:
  The processor loads on the Address bus the address of the memory location (Step 1).
    Some of the address lines select the memory devices that owns the memory location to be written (Step 1a), while the rest point to the required memory location within the memory device.
  The processor loads on the data bus the data to be written (Step 2).
  The processor activates the Write (WR) signal (Step 3).
    The data at the data bus is stored in the memory location specified by the address bus (Step 4).

## Slide 19: Address Decoding
The physical address space, or memory map, of a microprocessor refers to the range of addresses of memory location that can accessed by the microprocessor. The size of the address space depends on the number of address lines of the microprocessor.
At least two memory devices are required in a microprocessor system: one for the ROM and one for the RAM. In an 8086 the high addresses in the memory map should always be occupied by a ROM, while the low addresses in the memory map should always be occupied by a RAM. Address decoding is required in order to enable the connection of more than one memory devices on the microprocessor. Each device will occupy a unique area in the memory map.
A memory system is not fully decoded if some of the address lines are not used by the address decoding circuit or memory. In this case a memory device will occupy more than one sections in the memory map. This is referred as memory mirroring or memory imaging.

## Slide 20: Simplified memory map of 8086-DATS

## Slide 21: I/O Interfacing
Some microprocessors use the same address space for both memory and input/output devices. In this arrangement all instructions that are capable of accessing the memory locations can also access the input/output devices. This can be called Memory mapped I/O.
However, 8086 microprocessor permits the establishment of two separate address spaces for memory and input/output devices. Having separate address space for
the input/output devices is called direct I/O or Isolated I/O.

## Slide 22: Bus timing

## Slide 23: I/O instructions

## Slide 24: Address size expansion
More than one memory devices can be used to expand the number of memory locations on the system.
To expand the word size do the following:
  Determine the number of memory chips required, by dividing the required memory size with the size of the memory devices to be used.
  Connect the data lines of each memory chip in parallel on the data lines of the processor.
  Connect the address lines of each memory chip in parallel with the low address lines of the processor.
  Connect the CS lines of each memory device with the high address lines of the processor through an address decoding circuit..
  Connect together all WR and all RD lines of each memory device.

## Slide 25: Address Size Expansion: (32X4 RAM module using 8X4 RAM chips)
25

## Slide 26: Design an 8KX8 RAM module using 2KX8 RAM chips. The module should be connected on an 8-bit processor with a 16-bit address bus, and occupy the address range starting from the address A000. Show the circuit and the memory map.
26
Number of memory devices needed = 8K/2K = 4
Decoder needed = 2X4
Number of address lines on each 2KX8 memory chip = 11
2m = 2K = 21 x 210 = 211  (A0..A10)
Decoder needed = 2X4
 2 address lines are needed for the decoder.  (A11..A12)
Number of address lines needed for the address selection circuit
= 16 - 11 - 2 = 3  (A13, A14 A15)