## Slide 1: CEN 522: Topic 8 I/O
By Mr O. Omoruyi

## Slide 2: Input and Output
The input/output or I/O section allows the computer to take in data from the outside world. Peripherals such as keyboards, video display terminals, printers, Disk drive controller and modems are connected to the I/O section.
The actual physical devices used to interface the computer buses to external systems are often called ports. An input port allows data from a keyboard, an A/D converter, or some other source to be read into the computer under control of the CPU. An output port is used to send data from the computer to some peripheral, such as a video display terminal/ Screen, a printer, or a D/A converter.

## Slide 3: Input and Output (cont’d)
Physically, the simplest type of input or output port is just a set of parallel D flip-flops. If they are being used as an input port, the D inputs are connected to the external device, and the Q outputs are connected to the data bus which runs to the CPU. Data will then be transferred through the latches when they are enabled by a control signal from the CPU.
In a system where they are being used as an output port, the D inputs of the latches are connected to the data bus, and the Q outputs are connected to some external device. Data sent out on the data bus by the CPU will be transferred to the external device when the latches are enabled by a control signal from the CPU.

## Slide 4: I/O Ports
I/O devices are connected to the computer through I/O circuits. Each of these circuits contains several register called I/O Ports. Some are used for data while others are used control commands. Like memory locations, the I/O ports have address and they are connected to the bus system. These addresses are known as I/O address and can only be use in input (IN) or output (OUT) instructions.

## Slide 5: Input/Output Problems
Wide variety of peripherals
  Delivering different amounts of data
  At different speeds
  In different formats
All slower than CPU and RAM
Need I/O modules

## Slide 6: Input/Output Module
Interface to CPU and Memory
Interface to one or more peripherals

## Slide 7: Generic Model of I/O Module

## Slide 8: External Devices
Human readable
  Screen, printer, keyboard
Machine readable
  Monitoring and control
Communication
  Modem
  Network Interface Card (NIC)

## Slide 9: External Device Block Diagram

## Slide 10: I/O Module Function
Control & Timing
CPU Communication
Device Communication
Data Buffering
Error Detection

## Slide 11: I/O Steps
CPU checks I/O module device status
I/O module returns status
If ready, CPU requests data transfer
I/O module gets data from device
I/O module transfers data to CPU
Variations for output, DMA, etc.

## Slide 12: I/O Module Diagram

## Slide 13: I/O Module Decisions
Hide or reveal device properties to CPU
Support multiple or single device
Control device functions or leave for CPU
Also O/S decisions
  e.g. Unix treats everything it can as a file

## Slide 14: Input Output Techniques
Programmed
Interrupt driven
Direct Memory Access (DMA)

## Slide 15: Three Techniques for Input of a Block of Data

## Slide 16: Programmed I/O
CPU has direct control over I/O
  Sensing status
  Read/write commands
  Transferring data
CPU waits for I/O module to complete operation
Wastes CPU time

## Slide 17: Programmed I/O - detail
CPU requests I/O operation
I/O module performs operation
I/O module sets status bits
CPU checks status bits periodically
I/O module does not inform CPU directly
I/O module does not interrupt CPU
CPU may wait or come back later

## Slide 18: I/O Commands
CPU issues address
  Identifies module (& device if >1 per module)
CPU issues command
  Control - telling module what to do
    e.g. spin up disk
  Test - check status
    e.g. power? Error?
  Read/Write
    Module transfers data via buffer from/to device

## Slide 19: Addressing I/O Devices
Under programmed I/O data transfer is very like memory access
Each device given unique identifier
CPU commands contain identifier (address)

## Slide 20: I/O Mapping
Memory mapped I/O
  Devices and memory share an address space
  I/O looks just like memory read/write
  No special commands for I/O
    Large selection of memory access commands available
Isolated I/O
  Separate address spaces
  Need I/O or memory select lines
  Special commands for I/O
    Limited set

## Slide 21: Memory Mapped and Isolated I/O

## Slide 22: Interrupt Driven I/O
Overcomes CPU waiting
No repeated CPU checking of device
I/O module interrupts when ready

## Slide 23: Interrupt Driven I/O Basic Operation
CPU issues read command
I/O module gets data from peripheral whilst CPU does other work
I/O module interrupts CPU
CPU requests data
I/O module transfers data

## Slide 24: Simple Interrupt Processing

## Slide 25: CPU Viewpoint
Issue read command
Do other work
Check for interrupt at end of each instruction cycle
If interrupted:-
  Save context (registers)
  Process interrupt
    Fetch data & store

## Slide 26: Changes in Memory and Registers for an Interrupt

## Slide 27: Design Issues
How do you identify the module issuing the interrupt?
How do you deal with multiple interrupts?
  i.e. an interrupt handler being interrupted

## Slide 28: Identifying Interrupting Module (1)
Different line for each module
  PC
  Limits number of devices
Software poll
  CPU asks each module in turn
  Slow

## Slide 29: Identifying Interrupting Module (2)
Daisy Chain or Hardware poll
  Interrupt Acknowledge sent down a chain
  Module responsible places vector on bus
  CPU uses vector to identify handler routine
Bus Master
  Module must claim the bus before it can raise interrupt
  e.g. PCI & SCSI

## Slide 30: Multiple Interrupts
Each interrupt line has a priority
Higher priority lines can interrupt lower priority lines
If bus mastering only current master can interrupt

## Slide 31: Example - PC Bus
80x86 has one interrupt line
8086 based systems use one 8259A interrupt controller
8259A has 8 interrupt lines

## Slide 32: Sequence of Events
8259A accepts interrupts
8259A determines priority
8259A signals 8086 (raises INTR line)
CPU Acknowledges
8259A puts correct vector on data bus
CPU processes interrupt

## Slide 33: ISA Bus Interrupt System
ISA bus chains two 8259As together
Link is via interrupt 2
Gives 15 lines
  16 lines less one for link
IRQ 9 is used to re-route anything trying to use IRQ 2
  Backwards compatibility
Incorporated in chip set

## Slide 34: 82C59A Interrupt Controller

## Slide 35: Intel 82C55A Programmable Peripheral Interface

## Slide 36: Keyboard/Display Interfaces to 82C55A

## Slide 37: Direct Memory Access
Interrupt driven and programmed I/O require active CPU intervention
  Transfer rate is limited
  CPU is tied up
DMA is the answer

## Slide 38: DMA Function
Additional Module (hardware) on bus
DMA controller takes over from CPU for I/O

## Slide 39: Typical DMA Module Diagram

## Slide 40: DMA Operation
CPU tells DMA controller:-
  Read/Write
  Device address
  Starting address of memory block for data
  Amount of data to be transferred
CPU carries on with other work
DMA controller deals with transfer
DMA controller sends interrupt when finished

## Slide 41: DMA Transfer Cycle Stealing
DMA controller takes over bus for a cycle
Transfer of one word of data
Not an interrupt
  CPU does not switch context
CPU suspended just before it accesses bus
  i.e. before an operand or data fetch or a data write
Slows down CPU but not as much as CPU doing transfer

## Slide 42: DMA and Interrupt Breakpoints During an Instruction Cycle

## Slide 43: Aside
What effect does caching memory have on DMA?
What about on board cache?
Hint: how much are the system buses available?

## Slide 44: DMA Configurations (1)
Single Bus, Detached DMA controller
Each transfer uses bus twice
  I/O to DMA then DMA to memory
CPU is suspended twice

## Slide 45: DMA Configurations (2)
Single Bus, Integrated DMA controller
Controller may support >1 device
Each transfer uses bus once
  DMA to memory
CPU is suspended once

## Slide 46: DMA Configurations (3)
Separate I/O Bus
Bus supports all DMA enabled devices
Each transfer uses bus once
  DMA to memory
CPU is suspended once

## Slide 47: Intel 8237A DMA Controller
Interfaces to 80x86 family and DRAM
When DMA module needs buses it sends HOLD signal to processor
CPU responds HLDA (hold acknowledge)
  DMA module can use buses
E.g. transfer data from memory to disk
  Device requests service of DMA by pulling DREQ (DMA request) high
  DMA puts high on HRQ (hold request),
  CPU finishes present bus cycle (not necessarily present instruction) and puts high on HDLA (hold acknowledge). HOLD remains active for duration of DMA
  DMA activates DACK (DMA acknowledge), telling device to start transfer
  DMA starts transfer by putting address of first byte on address bus and activating MEMR; it then activates IOW to write to peripheral. DMA decrements counter and increments address pointer. Repeat until count reaches zero
  DMA deactivates HRQ, giving bus back to CPU

## Slide 48: 8237 DMA Usage of Systems Bus

## Slide 49: Fly-By
While DMA using buses processor idle
Processor using bus, DMA idle
  Known as fly-by DMA controller
Data does not pass through and is not stored in DMA chip
  DMA only between I/O port and memory
  Not between two I/O ports or two memory locations
Can do memory to memory via register
8237 contains four DMA channels
  Programmed independently
  Any one active
  Numbered 0, 1, 2, and 3

## Slide 50: I/O Channels
I/O devices getting more sophisticated
e.g. 3D graphics cards
CPU instructs I/O controller to do transfer
I/O controller does entire transfer
Improves speed
  Takes load off CPU
  Dedicated processor is faster

## Slide 51: I/O Channel Architecture

## Slide 52: Interfacing
Connecting devices together
Bit of wire?
Dedicated processor/memory/buses?
E.g. FireWire, InfiniBand

## Slide 53: Conclusion
Thank you.
References
Apeh, S. Lecture notes on Advanced Microcomputer systems, 2015