## Slide 1: CEN 522: Microprocessor Systems and Interfacing
Programming model in real mode
By
Omoruyi O.

## Slide 2: Topic
Registers,
Memory,
Addressing modes.

## Slide 3: Real mode programming model
A programming model is a view of the microprocessor that explains how the microprocessor sees and uses various components and tasks of the microprocessor system. This includes memory and registers in the microprocessor.
The real mode programming model of a microprocessor is an operating mode of x86( 8086 microprocessor family) compatible microprocessors.

## Slide 4: Real mode programming model
The real mode model is characterized by the following:
The 20 bit memory address space (allowing as much as (220 =1MB of memory space) Memory access is done using Segmentation via a segment: offset system.
Unlimited direct software access to all addressable memory, I/O addresses and peripheral hardware.

## Slide 5: Registers (8, 16, 32 and 64 bit) Fig. 3.1

## Slide 6: Registers explained
The programming model contains 8-, 16-, and 32-bit registers. The 8-bit registers are AH, AL, BH, BL, CH, CL, DH, and DL and are referred to when an instruction is formed using these two-letter designations. For example, an ADD AL,AH instruction adds the 8-bit contents of AH to AL. (Only AL changes due to this instruction.) The 16-bit registers are AX, BX, CX, DX, SP, BP, DI, SI, IP, FLAGS, CS, DS, ES, SS, FS, and GS. Note that the first four 16 registers contain a pair of 8-bit registers.
An example is AX, which contains AH and AL. The 16-bit registers are referenced with the two-letter designations such as AX. For example, an ADD DX, CX instruction adds the 16-bit contents of CX to DX. (Only DX changes due to this instruction.) The extended 32-bit registers are EAX, EBX, ECX, EDX, ESP,EBP, EDI, ESI, EIP, and EFLAGS. These 32-bit extended registers, and 16-bit registers FS and GS, are available only in the 80386 and above.

## Slide 7: Registers explained (64 bit)
The 64-bit registers are designated as RAX, RBX, and so forth. In addition to the renaming of the registers for 64-bit widths, there are also additional 64-bit registers that are called R8 through R15. The 64-bit extensions have multiplied the available register space by more than 8 times in the Pentium 4 and the Core2 when compared to the original microprocessor architecture as indicated in the shaded area in Figure 3–1.
An example of a 64-bit instruction is ADD RCX, RBX, instruction, which adds the 64-bit contents of RBX to RCX. (Only RCX changes due to this instruction.) One difference exists: these additional 64-bit registers (R8 through R15) are addressed as a byte, word, doubleword, or quadword, but only the rightmost 8 bits is a byte. R8 through R15 have no provision for directly addressing bits 8 through 15 as a byte. In the 64-bit mode, a legacy high byte register (AH, BH, CH, or DH) cannot be addressed in the same instruction with an R8 through R15 byte. Because legacy software does not access R8 through R15, this causes no problems with existing 32-bit programs, which function without modification.

## Slide 8: Real mode memory addressing
Only the 8086 and 8088 operate exclusively in the real mode. In the 64-bit operation mode of the Pentium 4 and Core2, there is no real mode operation. This section of the text details the operation of the microprocessor in the real mode.
Real mode operation allows the microprocessor to address only the first 1M byte of memory space—even if it is the Pentium 4 or Core2 microprocessor. Note that the first 1M byte of memory is called the real memory, conventional memory, or DOS memory system. The DOS operating system requires that the microprocessor operates in the real mode.

## Slide 9: Segments and Offset
A combination of a segment address and an offset address accesses a memory location in the real mode. All real mode memory addresses must consist of a segment address plus an offset address. The segment address, located within one of the segment registers, defines the beginning address of any 64K-byte memory segment. The offset address selects any location within the 64K byte memory segment. Segments in the real mode always have a length of 64K bytes.
Figure 3–2 shows how the segment plus offset addressing scheme selects a memory location. This illustration shows a memory segment that begins at location 10000H and ends at location IFFFFH—64K bytes in length. It also shows how an offset address, sometimes called a displacement, of F000H selects location 1F000H in the memory system. Note that the offset or displacement is the distance above the start of the segment, as shown in Figure 3–2.

## Slide 10: Segments and offset (fig. 3.2)

## Slide 11: Segment and offset registers
The microprocessor has a set of rules that apply to segments whenever memory is addressed. These rules, which apply in the real and protected mode, define the segment register and offset register combination. For example, the code segment register is always used with the instruction pointer to address the next instruction in a program. This combination is CS:IP or CS:EIP, depending upon the microprocessor’s mode of operation. The code segment register defines the start of the code segment and the instruction pointer locates the next instruction within the code segment. This combination (CS:IP or CS:EIP) locates the next instruction executed by the microprocessor. For example, if CS = 1400H and IP/EIP = 1200H , the microprocessor fetches its next instruction from memory location 14000H + 1200H or 15200H.

## Slide 12: Segment and offset registers (Stacks)
Another of the default combinations is the stack. Stack data are referenced through the stack segment at the memory location addressed by either the stack pointer (SP/ESP) or the pointer (BP/EBP). These combinations are referred to as SS:SP (SS:ESP), or SS:BP (SS:EBP).
For example, if SS = 2000H and BP = 3000H, the microprocessor addresses memory location 23000H for the stack segment memory location. Note that in real mode, only the rightmost 16 bits of the extended register address a location within the memory segment. In the 80386–Pentium 4,never place a number larger than FFFFH into an offset register if the microprocessor is operated in the real mode. This causes the system to halt and indicate an addressing error.

## Slide 13: Segment and offset register 16 & 32 bit (fig. 3.3)

## Slide 14: Addressing Mode
An addressing mode specifies how an operand required by an instruction is transferred to (or from) the CPU.
Common forms of addressing modes:
Register
Immediate or Literal
Direct
Register Indirect
Base or Displacement
Indexed

## Slide 15: Taxonomy of addressing modes (fig 3.4)

## Slide 16: Types of Addressing Mode
Register Addressing: the source/destination operand is a CPU register.
Immediate (Literal) Addressing: The operand is a part of the instruction fetched from memory.
Direct Addressing: The address of the operand is part of the instruction fetched from memory. In this mode the address is written in square brackets [address H] while H means that the address is written in Hexadecimal numbering system.
Register Indirect Addressing: The address of the operand is contained in a CPU register.
Base (Displacement) Addressing: The address is computed within the CPU by adding a value contained in a register to a base or displacement value. The base or displacement value is part of the instruction fetched from memory.
Indexed Addressing: The address is computed within the CPU by adding values contained in two CPU registers.

## Slide 17: Addressing Instructions and Data
An instruction consists of
– at least one operation -- ADD, MOVE, AND
– zero, one or more operands to reference the data
– Generally in Intel Microprocessors, the first operand is the destination
Example:
MOV AX,25 ; immediate operand
MOV AX,[0025H] ; direct addressing
MOV BX,AX ; register to register
MOV BX,[AX] ; indirect addressing

## Slide 18: Addressing Instructions and Data
– CS register contains the address of the beginning of a program’s code segment which contains instructions
– DS register contains the address of the beginning of a program’s data segment which contains data that instructions reference
– IP register indicates the offset address of the current instruction in the code segment to be executed
– Instruction operand indicates an offset address in the data segment to be referenced

## Slide 19: Conclusion
Thank you.

## Slide 20: References
The Intel Microprocessor, Architecture, Programming and Interfacing, 6th Ed., by Barr B Brey.
http://deeprajbhujel.blogspot.com/2015/12
/functional-block-diagram-of-8086.html
3. https://en.wikipedia.org/wiki/X86
4. https://en.wikipedia.org/wiki/Addressing_mode